## Slide 1: Localising the onset of face sensitivity in EEG time-series
Peter Hebden
Supervisor: Dr Guillaume Rousselet
12/8/2024
Image: Laurens R. Krol - Own work, CC0, https://commons.wikimedia.org

## Slide 2: Outine
Introduction​
Dataset​
Aims​
Methods​
Results​
Conclusion

## Slide 3: Introduction: EEG time series recorded during trials

## Slide 4: Dataset
The dataset of EEG recordings:
75 participants shown face and texture images,
each image presented for 104ms,
during two sessions,
up to 150 trials, and
up to 128 electrodes (Bieniek et al., 2016).
​
Image: Rousselet, et al., 2014)

## Slide 5: Aims
Detect face sensitivity ERP onset time from EEG recordings.
For each participant and each session:
  Evaluate methods for onset detection:
    cluster-based methods
    change point detection methods
  Evaluate impact of a data dimensionality reduction technique that builds a virtual electrode.

## Slide 6: Methods: cluster-based
Spatio-temporal cluster-based methods
  Cluster adjacent electrodes and time points (Bieniek et al., 2016).
Temporal cluster-based methods
  Cluster adjacent time points.
  Uses a virtual electrode of maximum t2 values (Rousselet, 2014).
Both methods
  Computationally expensive
  1000 permutations of every face and texture pair of trials.
  Use the cluster-sum method to detect the ERP onset.
                cluster-sum: a non-parametric statistical test (Maris & Oostenveld, 2007)
Notes: Both methods
  Computationally expensive
  Use the cluster-sum method to detect the ERP onset
              cluster-sum: a non-parametric statistical test (Maris & Oostenveld, 2007)
    1000 permutations of every face and texture pair of trials
    E.g., ~12.9 hours to estimate 150 onset times for the participants

## Slide 7: Methods: change point detection (CPD)
General purpose methods for detecting where an underlying process changes over time.
GFC
S&P 500 index
Why CPD methods?
  Fast (seconds or minutes)
    They do not use 1000s of permutations.
  Can set number of change points.
    Our data: one change point of interest.
Why not cluster-based methods?
  Slow (hours)
  Simulations have cast doubt on their accuracy (Sassenhagen & Draschow, 2019) .
  CPD methods have been suggested as an alternative (Rousselet, 2023).
    Binary segmentation (Scott & Knott, 1974).
    Other CPDs: Pelt, Window-based, Dynamic Programming, and BottomUp (in Python).

## Slide 8: Methods: participant virtual electrode
Build clusters:
(1) Find clusters of time points where
t2 > threshold.
(2) Sum t2 values for each cluster.
(3) Onset: 1st time point in 1st cluster
with cluster-sum > threshold.
Use permutations:
(1) define t2 threshold for time points.
Build a participant virtual electrode:
(1) t-test at each time point across all
electrodes.
(2) save ID of the max t2 electrode
for this participant.
participant VE
From the max t2 electrode
perms
onset

## Slide 9: Methods: session virtual electrode
Build a session virtual electrode:
(1) Use the average ERPs from the max t2 electrodes.
(2) Use permutations to set thresholds.
Build and test clusters:
Build clusters from adjacent t2 > threshold.
Find clusters with cluster-sum > threshold.
First time point in first significant cluster
is the ERP onset.
session VE
onset

## Slide 10: Results: onset predictions for each participant

## Slide 11: Results: ERP onset prediction for each session
Most predictions are consistent.​
Binseg predicts 72ms. ​
Temporal cluster-based predicts 76ms.​
Other CPD methods predicted later times.​

## Slide 12
Virtual electrodes make onset detection easier
  use the most relevant electrodes​,
  reduce dimensionality and increase SNR​,
  improve speed and accuracy​.
Accuracy of Binseg is similar to cluster-based methods ​
  when using one virtual electrode per particpant.​
Binseg and temporal CB methods predicted earlier onset times​
  when using one virtual electrode per session.​
A session virtual electrode built from max t2 electrodes ​ leverages the advantages of particpant virtual electrodes.
Conclusions

## Slide 14: Appendix
CPD cost functions
cost of each segment
  L1: least absolute deviation.
    sub = signal[start:end]
    med = median(sub)
    cost = abs(sub - med).sum()
  L2: least squared deviation
    cost = signal[start:end].var() * (end - start)
  normal: Gaussian process change
    sub = signal[start:end] # a vector, so use variance instead of covariance function.
    var = var(sub) # just a single value, not a square matrix in this case.
    val = slogdet(var) # compute the sign and natural log of the determinant of an array.
    cost = val * (end-start)
  rbf: Kernelized mean change
    uses a gram matrix

## Slide 15: Simulations indicated low accuracy
Cluster-based onset detections, synthetic data.
Image: (Sassenhagen and Draschkow, 2019)

## Slide 16: The cluster-sum method: distribution of max t2 values for participant 1
Distribution of cluster-sums t2 values for participant 1.
Distribution of t2 values for permutations of average face & texture ERPs of participant 1.
dist of max t2 values from permutations
dist of cluster sums
of clusters of
t2 values > threshold

## Slide 17: The cluster-sum method: distribution of cluster-sums for session 1
session virtual electrode
permutations of average
face & texture ERPs

## Slide 18: max t2 electrode counts and locations
Electrode B8 was the max t2 electrode 33 times.
An expected location for face sensitivity ERPs.
Top 6 are highlighted on the map:
B8=red, (B7, B9 ,B10)=orange, (A11, A28)=green.